Precision Farming Profitability

Reference A - Quiz

True/False Section:

- True/False:	The letters “GPS” stand for Global Positioning Survey.

- True/False:	Differential GPS or DGPS is needed to carry out site-specific farming

activities such as mapping yields, field boundaries, weedy areas, or soil sampling sites.

- True/False:	Differential GPS or DGPS is basically a “position locator” technique for

people, spreader trucks, sprayers, etc.

- True/False:	DGPS allows the user to get position estimates within 3-6 feet.

- True/False:	There are 24 orbiting GPS satellites and a minimum of 6-8 should be

available to the GPS receiver antenna at any point in time.

- True/False:	 A minimum of 4 satellites is required to compute a good three-

dimensional position.

- True/False:	Before differential correction was used, the most significant error was

intentional error.

- True/False: 	A different receiver is required for each job that uses GPS.

- True/False: 	Differential correction can compensate for all the errors associated with

the satellite clocks, orbits, and atmospheric-caused errors.

- True/False: 	Real-time DGPS is the most common form of DGPS being used for site-

specific farming activities.

Multiple Choice Section:

- GPS receiver (choose all that apply):

  - Receivers should have five or more tracking channels.

  - Receivers with more channels are more accurate.

  - All GPS receivers have the same number of channels and accuracy.

  - A different receiver is required for each job that needs a GPS.

  - Both a and b

- There are ____ orbiting GPS satellites and a minimum of _____ satellites should be directly visible to a GPS receiver at any point in time.

  - 20, 6-8

  - 22, 8-10

  - 24,6-8

  - 25, 8-10

- Signals from at least ___ satellites (minimum) are required to compute a “good” 3D position.

  - 2

  - 4

  - 6

  - 8

- Sources of error when not using Differential Correction:

  - Satellite clocks

  - Satellite orbits

  - Imperfection of GPS receivers

  - Earth’s atmosphere slows down the GPS signals

  - All of the above

- The indirect method for real-time GPS (choose the answer that does not apply):

  - Involves sending DC values to a geo-station satellite for re-broadcast

  - Does not provide a wider area of coverage than the direct method

  - May be less susceptible to “line-of-sight” interference

  - Costs includes subscription fee and an onboard receiver

- Which of these statements are incorrect (choose all that apply):

  - The magnitude of the standard deviation indicates the spread of a frequency distribution

  - A smaller standard deviation indicates a wider distribution

  - A smaller standard deviation indicates a narrower distribution

  - Root mean square (RMS) is approximately equivalent to standard deviation

- Circular Error Probable (CEP):

  - CEP is a statistical measure of accuracy that is sometimes used for a stationary situation

  - The error probable refers to the largest radius of a circle which will enclose 30% of computed positions over the short run

  - The error probable refers to the largest radius of a circle which will enclose 40% of computed positions over the long run

  - The error probable refers to the largest radius of a circle which will enclose 50% of computed positions over the long run

  - Both a and b

- The three possibilities for receiving DC values include all but one of the following:

  - Regional AM-like beacon services

  - Regional FM-like beacon services

  - Operate one’s own base station

  - Local FM or FM-sideband services

- Most Differential GPS receivers used in site-specific farming (choose all that apply):

  - Produce a position estimate within 5 meters of the “true” position estimate 68% of the time

  - Produce a position estimate within 1 meter of the “true” position estimate 68% of the time

  - Are within the sub-meter category

  - Are not in the sub-meter category

  - a, b, and c

- Accuracy in Site-Specific Farming GPS (choose all that apply):

  - For most current site-specific farming activities, the cost of centimeter accuracy is worth it.

  - Sub-meter accuracy is good enough for site-specific farming activities

  - Most Differential GPS receivers are in the sub-meter category

  - All of the above

  - Both b and c

True/False:

1. F, 2. T, 3. T, 4. T, 5. T, 6. T, 7. T, 8. F, 9. T, 10. T

Multiple Choice:

11. E, 12. C, 13. B, 14. E, 15. B, 16. B, 17. D, 18. B, 19. E, 20. E