Precision Farming Profitability

Reference B - Quiz

True/False Section:

- True/False:	Yield monitors are designed to obtain and record information for very

small harvest areas in a field.

- True/False:	The specified width is the harvested swath width.

- True/False:	Each unique location is specified by coordinates of latitude and longitude.

- True/False:	Yield monitors estimate the moisture content of the grain yield.

- True/False:	Harvest site yield is equal to grain volume divided by harvest site area.

- True/False:	The header position sensor tells the yield monitor to stop when it is

lowered and to start or continue when it is raised.

- True/False:	The yield monitor consol enables the operator to see monitor harvest data

as it is happening.

- True/False:	Data card and card slot are located in the on-board yield monitor system to

store mapping information.

- True/False:	The marking system enables the operator to physically mark the location

of special things observed during the harvest.

- True/False:	Grain volume is calculated from grain flow, moisture sensor data, and

standard bushel information.

Multiple Choice Section:

- Each harvest site has:

  - A specific width

  - A specific length

  - A unique location

  - All of the above

- Which of the following is a speed sensor type?

  - A magnetic sensor in the combine’s drive-train

  - Radar or sonar speed “gun”

  - The DGPS receiver on the combine

  - All of the above

- Prior to the initial harvest, the following must be set up within the yield monitor’s firmware:

  - Data logging interval

  - Preliminary calibration

  - None of the above

  - A and B

- The operator (choose all that apply):

  - Needs to electronically tag or label the yield monitoring data

  - Can change the pre-entered list from inside the cab

  - Uses real names for Field-Ids

  - All of the above

- Load-ID (choose all that apply):

  - A whole field can be tagged with a single Load-ID

  - Harvest passes can be given the same Load-ID

  - Load-IDs are used for investigating special in-field areas of concern

  - Use of Load-IDs does not significantly increase the management information potential of a yield monitoring system

  - a,b, and c

- Time delay (choose all that apply):

  - Time delay must be accounted for to get “geographically-correct” yield and moisture maps

  - It is safe to assume that harvest data is being recorded properly on the data card

  - Time delay is usually between 15-30 seconds depending on the combine make

  - Instant harvest data that is based on grain flow and moisture content will be current when displayed on the yield monitor console

- Yield summaries (choose all that apply):

  - Most yield monitors do not maintain an internal count of acres, grain amounts,  and harvest moisture for each Load-ID

  - Simple yield summaries are displayed on the in-cab console of some yield monitors

  - Yield summaries cannot be generated once harvest is completed

  - Yield summaries show load, crop and field totals

  - Both b and d

- Grain flow sensors (choose all that apply):

  - An impact force sensor estimates flow in bushels per second

  - An optical sensor estimates flow in bushels per minute

  - To estimate grain flow for immediate display, the yield monitor firmware uses an “electronic calibration curve”

  - To estimate grain flow for internal yield summaries, the yield monitor firmware uses an “electronic calibration curve”

  - Both c and d

- Calibrating grain moisture sensors:

  - All yield monitors use a capacitance-type moisture sensor

  - Even at low or high, capacitance-type moisture sensors are accurate moisture levels

  - Capacitance-type moisture sensors are sensitive to grain temperature

  - Capacitance-type moisture sensors are not sensitive to build up or coating of wet, sticky material on its metal surfaces

- Errors in grain yield estimates:

  - Accuracy of yield estimates depends on the accuracy of the grain quantity and harvest area estimates.

  - Grain yield is given as the area of the harvest site divided by the quantity of grain harvested from a given site

  - Grain yield is measured directly.

  - Well-calibrated flow rate and moisture sensors contribute to the accuracy of grain quantities used in yield calculations.

True/False:

1. T, 2. T, 3. T, 4. T, 5. F, 6. F, 7. T, 8. T, 9. F, 10. F

Multiple Choice:

11. D, 12. D, 13. D, 14. D, 15. E, 16. A, 17. E, 18. E, 19. C, 20. D